## Slide 1
RHD2164 Headstage 1 Board
0.550”
0.863”
FR406 material, 0.036” thick, ENIG (immersion gold) plating (2 μm)
No through-hole components; only SMDs
actual size
0.1” hole in corner

## Slide 2
Top Components (9 total)
3 pads not bonded
1 pad not bonded
R0: 0 Ω (0402)
R1: 100 Ω (0201)
R2: 100 Ω (0201)
R3: 100 Ω (0201)
C1: 0.1 μF (0402)
C2: 0.01 μF (0201)
RHD2164 bare die (7.3 mm x 4.2 mm, 0.20 mm thick)
85 total bondwires
Omnetics A79025 connector
Omnetics A79623 connector

## Slide 3
Bottom Components (1 total)
Omnetics A79025 connector

## Slide 4
Intan Technologies RHD2164 Bare Die
Approximately 4.2 mm
Approximately 7.3 mm
Red = glass openings for bond pads
Blue, Green = top metal layers (highly visible)
Gray = approximate outline of die (may vary from die to die due to variations in sawing)
Yellow Cross = center of design (may not coincide precisely with center of die due to variations in sawing)
Each die is 0.20 mm (8 mils) thick

## Slide 5
Bond Pad Dimensions
74.2 μm
116.0 μm
72.0 μm
30.2 μm
Bond pad metal: AlCu (99.5% aluminum, 0.5% copper)
Minimum bond pad pitch (center to center) on RHD2164: 101.6 μm (4.000 mil)